## Slide 1: Radiobiologic issues in the radiotherapy of non-Hodgkin’s lymphoma: a comparison between conventional radiotherapy and radioimmunotherapy in terms of BED to OARs
Pacilio M(1), Barone R(1), Betti M(1), Del Mastro C(2), Cicone F(3), Rauco R(1), Montani L(2), Monaco A(4), Chiacchiararelli L(2), Signore A(3), Mango L(1), Santini E(1), Scopinaro F(3)
(1) Medical Physics Department – S Camillo Forlanini Hospital – Rome
(2) Medical Physics Department – Sant’Andrea Hospital – Rome
(3) 2nd Faculty of Medicine – Sant’Andrea Hospital – “Sapienza“ University of Rome
(4) Radiotherapy Department – S Camillo Forlanini Hospital – Rome

## Slide 2: Introduction
Traditional therapeutic approach for non-Hodgkin lymphoma (NHL):
External beam radiotherapy (EBRT), alone or combined with chemotherapy
For recurrent and refractory B-cell NHLs, Radioimmunotherapy (RIT)
is promising therapeutic approach, to simultaneously treat multiple tumor sites throughout the body (including diffuse disease).
RIT delivers exponentially decaying continuous low dose rate RT (CLDR RT). LDR irradiation has great effectiveness on NHLs, whilst normal tissue should be better able to tolerate irradiation.
RIT with Yttrium-90 (90Y) ibritumomab tiuxetan (Zevalin®) combines the tumor targeting attributes of a monoclonal antibody against the CD20 antigen and the pure -radiation of 90Y (up to 2.2 MeV).

## Slide 3: Aims
To perform dosimetric studies in terms of BED to OARs and tumor, comparing relative effectiveness (RE) in RIT with RE in external beam radiotherapy (EBRT)
To compare BED to OARs with dose threshold for toxicity D5,5 of Emami, translated to BED3(D5,5) with conventional 2 Gy/fr regimen
To investigate on the possibility to increase administration and to reach dose prescriptions to tumor similar to EBRT ones.

## Slide 4: Materials and Methods
7 patients treated for NHL diffuse disease by 90Y-ibritumomab tiuxetan (Zevalin) at standard dosage (15 MBq/Kg)
OARs: liver, spleen, lungs, kidneys, heart walls, red marrow

## Slide 5
Biokinetic was assessed by 185 MBq of 111I-labeled antibody, administered before treatment as a “tracer”, by scintigraphic imaging performed from 10 min to 136 h after the administration
Transmission images were also acquired by 111In-flood source to perform attenuation correction.
Biokinetic studies for liver, spleen, lungs, kidneys, heart walls

## Slide 6
Biokinetic was assessed on the base of blood withdrawals, by Sgouros/AAPM model:
ARM/ABl = RMBLR mRM/mBl
ARM = RMBLR [A]Bl mRM
where the term RMBLR (red-marrow-blood-ratio) depends on red marrow extra cellular fluid fraction and the hematocrit value.
Biokinetic studies for red marrow
This model is valid under the assumptions of no binding to bone nor to marrow for whole antibodies.

## Slide 7
By CT acquisition and slice contouring on ADAC Pinnacle TPS, corrections for individual organ volume were applied to biokinetic data, moreover individual organ masses were calculated for dose assessment.
Internal dosimetry calculations are performed on the basis of the following input:
Biokinetic data
Organ volumes and masses
Whole body mass
Internal dosimetry calculations

## Slide 8
Internal dosimetry calculations
Dose calculations were performed by OLINDA/EXM software (FDA approved for internal dosimetry). The output is the mean physical dose absorbed by the organ.

## Slide 9: Radiobiology
LQ model and Lea-Catcheside factor
The generalized Lea-Catcheside factor G for a time-dependent dose-rate is given as follows:
G expresses the reduction in cell kill due to sublethal damage repair during continuous irradiation and/or between fractions

## Slide 10
EBRT
For fractionated RT, G = 1/n with n = number of fractions, so
RIT
RIT delivers exponentially decaying continuous-low-dose-rate RT (CLDR RT). With monoexponential clearance and 1 source organ
(complete tissue repair between fractions and negligible tumor repopulation)
(negligible tumor repopulation and incomplete tissue repair conditions)
where ln(2)/T1/2eff and  = ln(2)/T1/2REP are time-constants for radiopharmaceutical clearance and sublethal damage repair, respectively

## Slide 11
Generally, in radiopharmaceutical clearance, multi-exponential biokinetic + multiple source organ (for each target organ) are involved
More complicated expression for G
In RIT with 90Y-Zevalin, for liver, kidneys, lungs and spleen absorbed dose is due to single source (self-irradiation). In this work, biokinetic with uptake phase has been considered in radiobiological evaluations. Further calculation refinements for red marrow (2 source organ) are on going.
 | Liver, spleen, lungs, kidneys, heart-wall | Red marrow | Tumor
T1/2REP (h) | 0.5 ≤ T1/2REP ≤ 5 | 1.5 | 0.5
(Gy) | 3 | 10 | 10

## Slide 12: Results

## Slide 13: Results
BED (Gy3) | Liver | Kidneys | Lungs | Heart wall | Spleen
BED3 for T1/2REP=0.5 h | [6.2-9.0] | [3.8-6.1] | [1.5-5.3] | [3.6-13.3] | [2.9-6.9]
BED3 for T1/2REP = 3 h | [6.6-10.0] | [4.1-6.6] | [1.6-5.8] | [3.6-13.5] | [3.0-7.5]
BED3 for T1/2REP = 5 h | [6.9-10.7] | [4.3-7.0] | [1.6-6.2] | [3.6-13.6] | [3.1-8.0]
BED3(D5,5) | 50 | 38.3 | 29.2 | 66.7 | ---
BED3(D5,5)/BED3* | 4.7 | 5.5 | 4.7 | 4.9 | ---
Red marrow: 0.7 Gy10 ≤ BED10 ≤ 1.3 Gy10
Tumor: 12.3 Gy10 (our result), ~ 17 Gy (literature)
* The ratio was calculated for the maximum BED value
Tumor BED10 was quite similar to the physically absorbed dose, due to low RE value (1.01).

## Slide 14: Results
By considering EBRT dose prescription of about 36 Gy, corresponding to BED10  43.2 Gy10, Zevalin administration should be about 3.5-fold higher.
OAR BED have been re-calculated by varying the factor of dose increment (“dose factor”) in the range 2-3.5, to evaluate the tolerability of the treatment.
In RIT, toxicity threshold of 2 Gy (in terms of mean physical dose) is assumed for red marrow. By considering G = 1, maximum tolerable BED10 for red marrow is 2.4 Gy10.
In RIT dose increment involve dose-rate increment with consequent
RE increase due to reduced repair capacity of sublethal damages.

## Slide 15: Results
Dose factor = 1
1.001 ≤ RE ≤ 1.003 for red marrow, 1.06 ≤ RE ≤ 1.16 for other OARs

## Slide 16: Results
Dose factor = 2
1.002 ≤ RE ≤ 1.007 for red marrow, 1.11 ≤ RE ≤ 1.32 for other OARs
Toxicity

## Slide 17: Results
Dose factor = 3
1.003 ≤ RE ≤ 1.01 for red marrow, 1.17 ≤ RE ≤ 1.47 for other OARs
Toxicity
Toxicity
Toxicity

## Slide 18: Results
Dose factor = 3.5
1.007 ≤ RE ≤ 1.01 for red marrow, 1.19 ≤ RE ≤ 1.55 for other OARs
Toxicity
Toxicity
Toxicity
Toxicity

## Slide 19: Results
Dose factor = 3.5
1.30 ≤ RE ≤ 1.91 for OARs, mean value quite similar to EBRT one (1.67 for 2 Gy/fr)
Toxicity
Toxicity
Toxicity
Toxicity
Toxicity
Toxicity

## Slide 20: Conclusion
  Dosimetry and radiobiological evaluation are unavoidable in RIT with Zevalin at no standard dosages
  The factor of dose increment must be personalised on the basis of pre-treatment dosimetry
  BED calculations are affected by large uncertainties associated with radiobiological parameters
  However, BED calculations are useful guidance in treatment planning, considering also that combined treatment strategy (RIT + EBRT boost) may be necessary