## Slide 1: Rapid palliative symptomatic irradiation using helical tomotherapy preliminary analysis of workflow and feasibility at the Radiotherapy Department of Modena
1G. De Marco, 1M. Amadori, 1P. Antognoni, 1P. Giacobazzi, 2G. Guidi, 2E.Cenacchi, 1B. Lanfranchi, 1M. Parmiggiani, 1S. Pratissoli, 1S. Scicolone, 1F. Titone, 1G. Tolento, 2C. Danielli, 1F. Bertoni.
1 U.O. Radioterapia Oncologica, Azienda Ospedaliera Universitaria Policlinico di Modena; 2 Servizio di Fisica Sanitaria, Azienda Ospedaliera Universitaria, Policlinico di Modena;

## Slide 2: The rapid access palliative radiotherapy program: blueprint for initiation of a one stop multidisciplinary bone metastases clinic A. Fairchild et al.:Support Care Cancer 2009;17:163-170.
“Time is precious when life is short”
Aim of symptomatic palliative radiotherapy:
2 - Delivery of therapy and rapid access to care
1 - Symptom control
At Radiotherapy Department of Modena
palliative-symptomatic radiotherapy accounts for 22% of treatments
(ANNUAL REPORT 2008)

## Slide 3
Recent work has investigated the feasibility of online planning of palliative radiation therapy using kilovoltage cone-beam CT and external treatment planning and verify and record system

## Slide 4: TomoTherapy
The TomoTherapy Incorporated has developed
2 new software packages
for the tomotherapy Hi-Art treatment system for palliative treatment
StatRT (2007)
TomoDirect (2008)

## Slide 5: TomoDirect
Clinicians can choose several discrete angles and the optimal modulation level required for delivery,based on specific patient therapy goals.
This innovative new technology allows Hi-Art system users to quickly plan and deliver advanced TomoTherapy radiation treatments with a series of linear beam paths,rather than the existing helical path.

## Slide 6: StatRT
The software is designed to enhance the quality of care for time-critical cancer cases
StatRT saves precious time
StatRT is patient-centric
StatRT is versatility without compromise

## Slide 7
At the Radiotherapy Department of Modena a preliminary analysis of workflow and feasibility of rapid palliative irradiation with helical tomotherapy has been carryed out in a prospective series of symptomatic metastatic patients.
StatRT

## Slide 8: StatRT
3 - to evaluate the clinical benefit of employing a helical tomotherapy to scan, plan, and deliver a radiation treatment in a single radiotherapy appointment
1 - to establish the workflow
2 - to define the procedures
Aim

## Slide 9: StatRT material e methods
28.6% were re-treatments to previously irradiated cases
12 pts received RT to 1 single site and 2 pts were irradiated to 2 metastatic sites in a single treatment session
Distributions of palliation sites | 
Bone metastasis | 12
Rectal bleeding | 1
Lung metastasis | 1
re-treatments
March 2009-October 2009
14 consecutive pts (64% males,36% females; mean age: 67.7 years, range 48-95 yrs) with symptomatic metastasis have been prospectively accrued.

## Slide 10
Fractionation regimens
Distribution of total doses delivered
StatRT - material and methods
n. pts

## Slide 11
Patient positioning on the treatment couch
Megavoltage CT(MVCT) of 3.5 MV with Slice thikness 2 mm
Acquisition of superior/inferior borders encompassing the intended treatment volume
Contouring of GTV and GTV to PTV uniform expansion of 1 cm
StatRT - material and methods
Optimization planning
Calculation grid 0.4 mm
MF 1.2
Iterations max 10
Pitch 0.287
Field Width 5 cm

## Slide 12
Delivery Quality Assurance (DQA) was performed for the first 3 patients, after the treatment session.
γ INDEX is within 3 mm and 3%(*)
StatRT - material and methods
(*) ISTISAN 2009

## Slide 13
ENDPOINTS
Times necessary for each treatment phase have been registered
Patient compliance evaluated by creating an arbitrary index score
Conformity index (CI) and OARs and PTV dose distributions performed by dosimetry comparison with a conventional 3D-CRT
StatRT - material and methods

## Slide 14
Set-up
MVCT
Contouring
Plan calculation
Irradiation delivery
StatRT - material and methods
Times
IN – OUT
for each patient treated

## Slide 15
Patient compliance
For each treated patient an arbitrary index score
was created.
1 | good
2 | fair
3 | poor
StatRT - material and methods

## Slide 16
Conformity index (CI) and OARs and PTV dose distributions
In 3 patients a dosimetry comparison of statRT treatment vs conventional 3D-CRT was performed evaluating
  CI
  OARs and PTV dose distributions
StatRT - material and methods

## Slide 17
Times
Mean overall treatment time (IN-OUT) was 106.3 min. Range: 48 - 180
StatRT - results
TIME IN MINUTES
PATIENT NUMBER
Notes: <number>

## Slide 18
Times
StatRT - results

## Slide 19
Patient compliance
StatRT - results

## Slide 20
Fig. 3: PdT e DVH calcolati per 3D-CRt con LINAC 18 MV
Fig. 4: PdT e DVH calcolati per Tomoterapia
Conformity index (CI) and OARs and PTV dose distributions
StatRT - results
Notes: <number>
Papillon: tecnica isocentrica ad arco con 60Co 30 in fr. Sul T

## Slide 21
Dose Index comparison of (a) STAT-RT and (b) 3D-CRT |  |  |  | 
V95 Dp | (a) 1 | 97,93% | (b) 1 | 96,92%
DM polmone sin |  | 5,47 Gy |  | 5,8 Gy
DM polmone dx |  | 1,1 Gy |  | 0,2 Gy
DMAX midollo |  | 11,5 Gy |  | 13,84 Gy
CI |  | 0,024 |  | 0,005
V95 Dp | (a) 3 | 99.99% | (b) 2 | 86.28%
DMAX midollo |  | 7.29 Gy |  | 8.09 Gy
DMAX esofago |  | 7.26 Gy |  | 6.67 Gy
DM polmone dx |  | 1.56 Gy |  | 1.32 Gy
DM polmone sin |  | 1.41 Gy |  | 0.93 Gy
CI |  | 0.012 |  | 0.006
V95 Dp | (a) 3 | 98,62% | (b) 3 | 91,05%
DM Intestino |  | 3.55 Gy |  | 3.674 Gy
CI |  | 0.01 |  | 0.006
Conformity index (CI) and OARs and PTV dose distributions
StatRT - results

## Slide 22: StatRT - Conclusion
TO DEFINE ORGANIZATIONAL PROCEDURES AND THE COSTS/BENEFITS RATIO
  Compliant patients
  Re-treatments after previous palliative RT
  Training of operators